## Slide 1: Electronics Presentation
AIITRA ‘21

## Slide 2: Sensors Microcontroller
IMU
Component chosen : MPU6050
Purpose : To get the accurate position as well as orientation of the bot at all times
LIDAR
Component chosen : TF-LUNA Micro LiDAR
Purpose : to map and understand the environment around the bot
Component chosen : ESP32 WROOM board
Purpose : To obtain all the sensor data and publish to the ros core running on the local machine and give instructions to the motors and controllers.

## Slide 3: Electronics and Power
BATTERY PACK
A battery pack consisting of 4 LG HG-2 18650 3000 mAh Li-ion batteries
Aspects considered :
  Provide enough power to all components
  Should last long enough for one clean without having to recharge in middle
  Minimum calendar ageing
MOTORS
DC Gear Motor
  Component Chosen : RS-540SH-5045
  Purpose : To drive the wheels
DC Motor - Fan
  Component Chosen : 12V - 3000 RPM DC
  Purpose : to run the vacuum fan

## Slide 4: Manufacturability
Component | Manufacturer | Procurement in India | Component Testing
MPU 6050 | InvenSense | Mouser Electronics | Basic Calibration (using Adafruit Library)
TF-LUNA Micro LiDAR | Benewake | Robu.in | Elementary software testing (using the Serial library)
ESP-32 WROOM board | Espressif | Robu.in | Unit tests (using the ESP-IDF)
LG HG2 18650 Cells | LG | Battery Bro | Capacity tests and CCD tests
DC Motors | Kysan Electronics | Kysan Electronics | Direct testing to find temperature and efficiency

## Slide 5: FMEA
Damaged Sensors
CAUSE : The IMU and Lidar might get damaged due to constant exposure to water and other fluids.
EFFECT : Decrement in accuracy and total non-working in case of severe damage
DETECTION :
ACTION : If one sensor is damaged, the sensor fusion algorithm detects a significant amount of discrepancy in the values obtained from two sensors.
Erroneous Navigation
CAUSE : The cumulative errors in the position of the bot leads to a significant deviation from the intended path
EFFECT : Fallacious values being fed into the path planning algorithm further reducing the efficiency of bot
ACTION : The following solutions are proposed :
  Implementation of an Extended Kalman filter algorithm to fuse the sensor data obtained from inertial measurement unit and LIDAR. ( Can be achieved via ROS Packages)
  Setting up a Proportional-Integral-Derivative controller in the navigation ROS stack to fine tune the control.

## Slide 6
Abnormal Temperature
CAUSE : Due to overload and continuous operations, the Lithium batteries might get over-discharged
EFFECT : Significant risk of abnormal temperatures and the batteries getting exploded
DETECTION : The internal temperature sensors monitor the temperature of the batteries and the system continuously
ACTION : The battery pack comes with a BMS which should handle this case forcing a shutdown of the power circuit. Further to prevent reaching abnormal temperatures, a proper ventilation system is considered while designing the model.