## Slide 1: ROBOT DESIGN

## Slide 2: Ideation
The key factors taken into consideration while design the robot were:
Dimension Constraints
Cleaning Efficiency
Equipment Onboard
  Electrical equipment
  Cleaning equipment
Mobility
Taking into consideration the above factors, the robot was designed to be of a disk shape for better maneuvering with two rotating brushes on the sides for increasing cleaning area and efficiency.The wheel placement was decided by triangulation method to provide more room at the front for a higher sweeping area for the brushes.

## Slide 3: Manufacturability
Body and Bin
  The material being used for the body and the bin of the robot is ABS (Acrylonitrile butadiene styrene). ABS is widely used for the following reasons:
    Its cheap
    Easy to manufacture
    Can injection molded
Brushes
  The brushes are an integral part of the robot and play an important role in cleaning. They need to be very strong as they are needed to rotate at very high RPM but at the same time flexible enough to scrape the floor efficiently and also not hinder in the mobility of the robot. The brushes used are of nylon to provide necessary strength and flexibility.

## Slide 4: Serviceability
Since we expect the robot to function in a dirty environment, the mechanical parts used need regular maintenance for optimum performance and need to be replaced after a certain period of time.
PART | CLEANING FREQUENCY | REPLACEMENT FREQUENCY
BIN | AFTER EVERY USE | –
BRUSHES | AFTER EVERY 5 USES | AFTER 180 USES
FILTER | AFTER EVERY 5 USES | AFTER 50 USES
FRONT CASTER WHEEL | AFTER EVERY 10 USES | –

## Slide 5: Failure Cases
Material Failure
  The body has been designed with an appropriate quantity of ABS plastic to handle the weight of the components and the high torques developed.
Contamination
  Vacuum fan
  Motors
  Electrical components
Re-dispositon